## Slide 1
Hochschule München University of Applied Sciences
Master Thesis Defense
Computational Engineering (M.Sc.)
Heykel Khadhraoui
Design and Implementation of a Real-Time Impedance Controller for a 7-DOF Collaborative Robot
Passive contact-induced alignment of a rectangular grinding tool on a planar surface
Supervisors: Prof. Norbert Nitzsche · Prof. Ruth Otto
2026

## Slide 2
Motivation
Angular mismatch at contact entry can create edge-first contact and high local loads
Design and Implementation of a Real-Time Impedance Controller for a 7-DOF Collaborative Robot
Master Thesis · Heykel Khadhraoui
1
Problem
• Surface placement, tool mounting and pose tolerances produce a small angular mismatch before contact.
• A rigid pose controller resists the corrective rotation generated at the leading edge or corner.
Desired behaviour
• Maintain the commanded normal press.
• Allow contact interaction to rotate the tool passively towards the surface.
7 DOF
Franka Emika Panda
1 kHz
torque-control loop
69
reported trials

## Slide 3
Research objective and contribution
What the controller should achieve and what the experiments measure
Design and Implementation of a Real-Time Impedance Controller for a 7-DOF Collaborative Robot
Master Thesis · Heykel Khadhraoui
2
Main question
How do directional stiffness and the position of the virtual centre of compliance influence passive tool alignment during Contact Establishment?
Primary measured response
γₜ₁ — signed end-effector rotation about the first surface tangent during Contact Establishment
Contributions
• Real-time Cartesian impedance controller with surface-relative stiffness and damping.
• Shiftable virtual centre of compliance that couples translation and rotation.
• Experimental comparison of rotational stiffness, translational stiffness and CoC position.
• Separate evaluation of projected null-space damping and singular-value conditioning.

## Slide 4
Controller concept
Cartesian impedance in the surface frame and torque-level implementation
Design and Implementation of a Real-Time Impedance Controller for a 7-DOF Collaborative Robot
Master Thesis · Heykel Khadhraoui
3
Cartesian impedance
Joint-torque command
• The desired orientation is held during Contact Establishment.
• Finite rotational compliance lets the measured contact moment generate the observed rotation.
The controller does not prescribe an additional alignment trajectory.

## Slide 5
Virtual centre of compliance
A tangential CoC displacement turns the normal press into a direction-selective moment
Design and Implementation of a Real-Time Impedance Controller for a 7-DOF Collaborative Robot
Master Thesis · Heykel Khadhraoui
4
Small-angle direction used for the general selection rule
• u gives the first-order direction of the combined small rotations about t₁ and t₂.
• r₍c,t₎ is selected perpendicular to u in the surface tangent plane.
• With Fₙ < 0 during pressing, the resulting contribution acts opposite to u and supports reduction of the offset.

## Slide 6
Experimental setup and procedure
The contact experiment isolates one parameter at a time while retaining the same geometry and state sequence
Design and Implementation of a Real-Time Impedance Controller for a 7-DOF Collaborative Robot
Master Thesis · Heykel Khadhraoui
5
1
Tool Orientation
→
2
Surface Approach
→
3
Contact Establishment
→
4
Pre-Grinding Hold
Common Contact Establishment settings
• Normal pressing trajectory along −nₛ.
• Orientation reference held at the measured entry orientation.
• Low rotational stiffness about t₁ and t₂; higher stiffness about nₛ.
• Three repetitions per parameter setting.
Main cases
A: TCP baseline · B: Kᴿ,ₜ₁ · C: Kᵖ,ₜ₂ · D: rᶜ,ₜ₂

## Slide 7
Results I — baseline and stiffness effects
Cases A–C show which controller parameters most strongly change the contact response
Design and Implementation of a Real-Time Impedance Controller for a 7-DOF Collaborative Robot
Master Thesis · Heykel Khadhraoui
6
Case A
TCP-centred baseline
Case B
63.9% lower response from 5 to 50 N m/rad
Case C
Only 0.4% response span across the tested Kᵖ,ₜ₂ range
Takeaway: the alignment response is much more sensitive to rotational stiffness than to the tested tangential translational stiffness.

## Slide 8
Results II — tangential CoC position
Case D is the main compliance-centre result
Design and Implementation of a Real-Time Impedance Controller for a 7-DOF Collaborative Robot
Master Thesis · Heykel Khadhraoui
7
What changes with rᶜ,ₜ₂?
• For the positive initial offset, increasing rᶜ,ₜ₂ increases the measured alignment response.
• For the negative initial offset, the same displacement direction progressively suppresses the response.
• A suitably selected displacement increased the final response by about 4%.
• The opposite displacement direction reduced the response by approximately 98–99%.
Main interpretation
The displaced CoC acts mainly as a selector of the preferred rotational direction.

## Slide 9
Why the CoC position changes the response
The normal press is converted into an additional TCP moment through the virtual lever arm
Design and Implementation of a Real-Time Impedance Controller for a 7-DOF Collaborative Robot
Master Thesis · Heykel Khadhraoui
8
Physical interpretation
• At the TCP, rᶜ = 0 and the CoC-induced moment vanishes.
• A tangential displacement creates a lever arm relative to the normal pressing force.
• Reversing the displacement reverses the sign of the additional moment.
• Therefore the same normal press can support one rotational direction and oppose the other.
This explains the strong sign dependence measured in Case D.

## Slide 10
Secondary study — null-space pose hold
Projected damping and singular-value conditioning were evaluated separately
Design and Implementation of a Real-Time Impedance Controller for a 7-DOF Collaborative Robot
Master Thesis · Heykel Khadhraoui
9
Projected damping
Cumulative projected null-space motion reduced by about 25%.
Singular-value conditioning
Net displacement reduced by about 99.8–99.9% for the tested disturbance direction.
Trade-off
The larger conditioning torque produced more back-and-forth motion although the final net displacement remained near zero.

## Slide 11
Main conclusions
What the experimental results establish
Design and Implementation of a Real-Time Impedance Controller for a 7-DOF Collaborative Robot
Master Thesis · Heykel Khadhraoui
10
1
A real-time Cartesian impedance controller produced passive contact-induced rotation towards the configured surface.
2
Rotational stiffness strongly affected the response; the tested tangential translational stiffness had only a minor effect.
3
The virtual CoC mainly selected the preferred rotational direction by changing the additional TCP moment generated during pressing.
4
The TCP-centred CoC is direction-independent and is therefore a suitable final configuration after alignment.
5
The results motivate an adaptive strategy: detect the initial tilt direction, temporarily select the tangential CoC displacement, then return the CoC to the TCP.

## Slide 12
Limitations and future work
Scope of the present results and the next development steps
Design and Implementation of a Real-Time Impedance Controller for a 7-DOF Collaborative Robot
Master Thesis · Heykel Khadhraoui
11
Limitations
• One robot configuration, one rectangular tool and one planar surface.
• Physical tool–surface angle was not measured directly during contact.
• Tool-mount compliance can make the physical tool-face rotation differ from the measured end-effector rotation.
• The null-space study used one disturbance direction.
Future work
• Measure the physical tool–surface angle and interaction wrench more directly.
• Implement online selection of the tangential CoC direction from the measured initial angular mismatch.
• Return the CoC to the TCP after alignment to remove the directional bias.
• Extend the evaluation to additional surfaces, tool geometries and real grinding trajectories.

## Slide 13
Conclusion
The virtual centre of compliance is a direction-selective design parameter for passive alignment
Design and Implementation of a Real-Time Impedance Controller for a 7-DOF Collaborative Robot
Master Thesis · Heykel Khadhraoui
12
The key result
A displaced CoC does not simply “increase compliance”. It creates a preferred rotational direction through the moment rᶜ × f.
For unknown initial misalignment, the direction should therefore be selected from the measured angular-offset direction rather than using one fixed non-zero tangential displacement.
Thank you
Questions and discussion