## Slide 1
Hochschule München University of Applied Sciences
Fakultät für Maschinenbau Fahrzeugtechnik Flugzeugtechnik
Master Thesis Defense
Computational Engineering (M.Sc.)
Heykel Khadhraoui
Design and Implementation of a Real-Time Cartesian Impedance Controller for a 7-DOF Collaborative Robot
Contact-induced alignment of a grinding tool with a plane surface
Supervisors: Prof. Norbert Nitzsche · Prof. Ruth Otto
2026

## Slide 2
Motivation and research question
Contact begins with an angular mismatch between tool and surface
Problem
Edge- or corner-first contact can create a moment while a rigid pose controller resists the corrective rotation.
Question
How do directional Cartesian stiffness and a virtual centre of compliance shape the contact-induced rotation?
Goal: press against the surface while allowing the tool to rotate towards alignment.
Design and Implementation of a Real-Time Cartesian Impedance Controller
Master Thesis - Heykel Khadhraoui
2

## Slide 3
Real-time Cartesian impedance controller
One torque command combines the Cartesian task and the secondary null-space terms
τ_cmd = JᵀF + τ_null + τ_c(q,q̇)
Three design elements
• Directional stiffness and damping in the surface frame.
• Shiftable virtual centre of compliance.
• Projected null-space damping / conditioning.
1 kHz
nominal torque callback
7 DOF
Franka Panda
Design and Implementation of a Real-Time Cartesian Impedance Controller
Master Thesis - Heykel Khadhraoui
3

## Slide 4
Virtual centre of compliance
The normal press can generate an additional corrective moment
m = m_R + r_c × f
• r_c = 0: no directional CoC moment.
• Tangential r_c: the normal press creates a moment about a surface tangent.
• Reversing r_c reverses that moment.
The useful CoC direction therefore depends on the direction of the initial angular offset.
Design and Implementation of a Real-Time Cartesian Impedance Controller
Master Thesis - Heykel Khadhraoui
4

## Slide 5
Experimental setup and contact sequence
The quantitative evaluation focuses on Contact Establishment
Contact Establishment
The tool approaches to a 20 mm geometric clearance and then presses toward the plane while the entry orientation is held.
Measured response: end-effector rotation during this phase.
All surface-contact comparisons use the same geometry and phase sequence.
Design and Implementation of a Real-Time Cartesian Impedance Controller
Master Thesis - Heykel Khadhraoui
5

## Slide 6
Experimental plan
Cases A–D isolate baseline, stiffness effects, and compliance-centre position
A
TCP-centred baseline
initial offset direction
B
Rotational stiffness
K_R,t₁
C
Tangential stiffness
K_p,t₂
D
Tangential CoC position
r_c,t₂
3×
repetitions / setting
57
surface-contact trials
12
pose-hold trials
69 reported trials in total.
Design and Implementation of a Real-Time Cartesian Impedance Controller
Master Thesis - Heykel Khadhraoui
6

## Slide 7
Results — baseline and stiffness
Rotational stiffness changes the alignment response much more than tangential translational stiffness
TCP centred
K_R,t₁: 5 → 50 N·m/rad
K_p,t₂: 300 → 2000 N/m
−63.9%
response with higher rotational stiffness
0.4%
response span from K_p,t₂ sweep
The contact response is much more sensitive to rotational stiffness about the response axis.
Design and Implementation of a Real-Time Cartesian Impedance Controller
Master Thesis - Heykel Khadhraoui
7

## Slide 8
Results — tangential CoC position
The same lever direction assists one initial offset and opposes the other
Positive initial offset
−40 → +40 mm
γₜ₁: 0.18° → 7.87°
Negative initial offset
−40 → +40 mm
γₜ₁: −11.30° → −0.09°
Opposite CoC direction reduced the response by ≈98–99%.
Direction matters more than simply increasing stiffness.
Design and Implementation of a Real-Time Cartesian Impedance Controller
Master Thesis - Heykel Khadhraoui
8

## Slide 9
Why the CoC changes the response
The normal force stays similar while the commanded moment changes strongly
Positive-offset comparison
−77…−82 N
steady normal force
+3.28 → −2.44 N·m
TCP moment across ±40 mm CoC
The displaced CoC mainly changes the rotational moment generated by the press, not the press magnitude.
Design and Implementation of a Real-Time Cartesian Impedance Controller
Master Thesis - Heykel Khadhraoui
9

## Slide 10
Secondary null-space result
The Cartesian pose is held while redundant joint motion is shaped separately
Projected damping
≈25%
less cumulative null-space motion
Conditioning
0.015° / 0.006°
final |Δη| at 1.5 / 2.0 N·m
Cartesian position stayed below the 2 mm acceptance limit.
Design and Implementation of a Real-Time Cartesian Impedance Controller
Master Thesis - Heykel Khadhraoui
10

## Slide 11
Main findings
Three results answer the contact-alignment question
1
Rotational compliance enables contact-induced alignment.
Higher rotational stiffness strongly reduces the response.
2
A displaced CoC is direction-selective.
Its lever can assist or oppose the required rotation.
3
The TCP-centred CoC is direction-independent.
It removes the additional directional moment after alignment.
Practical strategy: use a temporary direction-selected CoC, then return the CoC to the TCP.
Design and Implementation of a Real-Time Cartesian Impedance Controller
Master Thesis - Heykel Khadhraoui
11

## Slide 12
Limitations
The quantitative results are scoped to the tested hardware and geometry
Measurement
Physical tool–surface angle and contact centre were not measured directly.
Experimental scope
One robot configuration, tool, surface reference, and contact trajectory.
Tool mount
About ±2° unloaded play can make the physical tool motion differ from the measured EE rotation.
The reported percentages describe the investigated parameter ranges, not a universal robot/tool optimum.
Design and Implementation of a Real-Time Cartesian Impedance Controller
Master Thesis - Heykel Khadhraoui
12

## Slide 13
Future work
Adaptive temporary CoC based on the measured initial offset
1
Start at TCP
2
Estimate offset
3
Apply selected lever
4
Return to TCP
• Direct tool-angle / force–torque measurement.
• More directions in the surface tangent plane.
• Combined null-space terms under physical disturbances.
Design and Implementation of a Real-Time Cartesian Impedance Controller
Master Thesis - Heykel Khadhraoui
13

## Slide 14
Conclusion
Final answer to the contact-alignment question
A real-time Cartesian impedance controller was implemented and tested on the Franka Panda.
Rotational stiffness controls how freely contact can rotate the tool.
The virtual CoC controls which rotational direction the press favours.
Best practical interpretation: temporary selected lever → TCP-centred compliant contact.
Thank you
Questions
Design and Implementation of a Real-Time Cartesian Impedance Controller
Master Thesis - Heykel Khadhraoui
14

## Slide 15
Backup — surface frame and response metric
Signed quantities used for the contact comparison
BACKUP
γₜ₁ and θ_init,t₁ have the same sign when the measured rotation is toward the configured surface-parallel orientation.
Design and Implementation of a Real-Time Cartesian Impedance Controller
Master Thesis - Heykel Khadhraoui
15

## Slide 16
Backup — Cartesian impedance equations
Surface-relative translational and rotational impedance
BACKUP
m = Kᴿ eᴿ − Dᴿ ω_EE
During Contact Establishment the entry orientation is held as the reference; the later end-effector rotation is therefore the measured contact response.
Design and Implementation of a Real-Time Cartesian Impedance Controller
Master Thesis - Heykel Khadhraoui
16

## Slide 17
Backup — CoC transformation
Point-shift formulation used by the controller
BACKUP
Design and Implementation of a Real-Time Cartesian Impedance Controller
Master Thesis - Heykel Khadhraoui
17

## Slide 18
Backup — complete controller state flow
Program-level operating modes and common stop paths
BACKUP
Design and Implementation of a Real-Time Cartesian Impedance Controller
Master Thesis - Heykel Khadhraoui
18

## Slide 19
Backup — tool geometry and calibration
Clearance, leading feature, and configured surface reference
BACKUP
• Tool face: 40 × 120 mm; tool-centre offset: 20 mm.
• Approach ends when the minimum face clearance reaches 20 mm.
• The surface and tool-normal calibrations define the orientation metrics.
Design and Implementation of a Real-Time Cartesian Impedance Controller
Master Thesis - Heykel Khadhraoui
19

## Slide 20
Backup — main gains and timings
Values held constant unless explicitly varied
BACKUP
Orientation / approach
• K_p = [150,150,150] N/m
• K_R = [180,180,90] N·m/rad
• ζ = 1.9; approach = 0.1 m/s
Contact Establishment
• Baseline K_p = [2000,2000,350] N/m
• Baseline K_R = [5,5,50] N·m/rad
• ζ = 1.0; press = 0.08 m/s; timeout = 5 s
Surface-contact null space
• d_null = 2 N·m·s/rad
• k_σ = 1 N·m
• fixed across Cases A–D
Each parameter setting was repeated three times.
Design and Implementation of a Real-Time Cartesian Impedance Controller
Master Thesis - Heykel Khadhraoui
20

## Slide 21
Backup — surface-contact experimental matrix
Cases A–D and tested values
BACKUP
Case
Variable
Tested values
Trials
A
TCP-centred baseline
φ₀=0.74°; +9.31°; −9.41° about t₁; r_c=0
9
B
Rotational stiffness
K_R,t₁ = 15, 50 N·m/rad (+5 baseline)
6
C
Tangential translational stiffness
K_p,t₂ = 300, 800 N/m (+2000 baseline)
6
D
Tangential CoC position
r_c,t₂ = −40, −20, −10, +10, +20, +40 mm (+0 baseline)
36
Design and Implementation of a Real-Time Cartesian Impedance Controller
Master Thesis - Heykel Khadhraoui
21

## Slide 22
Backup — null-space controller and pose-hold test
Projected damping and singular-value conditioning
BACKUP
• 4 settings × 3 trials.
• 20 N virtual disturbance on link 3.
• Cartesian acceptance: max ||e_p|| < 2 mm.
Design and Implementation of a Real-Time Cartesian Impedance Controller
Master Thesis - Heykel Khadhraoui
22

## Slide 23
Backup — software, safety, and logging
Implementation details for reproducibility
BACKUP
Software
• Ubuntu 20.04.3 + PREEMPT_RT
• C++14 / Eigen 3.3.7
• libfranka 0.7.1
Real-time handling
• Preallocated callback data
• Keyboard input on separate thread
• CSV write after torque control
Robot-side monitoring
• Robot errors/reflexes terminate control
• Collision thresholds remain robot-side
• Gravity compensation handled by FCI
Signals are logged at the nominal 1 kHz controller rate.
Design and Implementation of a Real-Time Cartesian Impedance Controller
Master Thesis - Heykel Khadhraoui
23

## Slide 24
Backup — numerical result summary
Key values for questions
BACKUP
Comparison
Reference / low
Changed / high
Measured effect
Case A, + offset
θ_init=+9.31°
γ=+7.57°
81.3% of initial magnitude
Case A, − offset
θ_init=−9.41°
γ=−10.83°
115.1% of initial magnitude
Rotational stiffness
K_R,t₁=5 → γ=7.57°
K_R,t₁=50 → γ=2.73°
63.9% reduction
Translational stiffness
K_p,t₂=300 → γ≈7.56°
K_p,t₂=2000 → γ≈7.57°
0.4% span
CoC, + offset
−40 mm → 0.18°
+40 mm → 7.87°
direction-selective
CoC, − offset
−40 mm → −11.30°
+40 mm → −0.09°
direction-selective
Projected damping
E_N=7.596°
E_N=5.687°
≈25% less cumulative motion
Conditioning 1.5 / 2.0
|Δη|=0.015°
|Δη|=0.006°
very small final displacement
Design and Implementation of a Real-Time Cartesian Impedance Controller
Master Thesis - Heykel Khadhraoui
24